## Slide 1
Welding Manipulators Path Planning
R36094189 Yu-En Shen
Notes: Good afternoon, teacher and classmates. I’m Yu-En Shen, today I will introduce about my project.
My topic is about planning the path of the welding manipulators in car production line.

## Slide 2
CONTENTS
01
Problem Description
02
Parameters & Variables
03
Model Design
04
Results
Notes: My presentation has four chapters.
The first is to describe problem
The following chapter will introduce about the problem in reality and some parameters and variables.
Then I will introduce the model design and conclude the presentation.
Finally show the result solved by gurobi

## Slide 3
Problem Description
01
Notes: The next chapter is problem description.

## Slide 4
Welding points around a car
Problem Description
Introduction about this problem
Notes: I want to make manipulators welding car shell.
There are many welding points around a car, and we need to weld all points.
Because different manipulators can weld at the same time, our objective is to minimize the max processing time of manipulators, instead of the total processing time

## Slide 5
Welding points around a car
Problem Description
Introduction about this problem
Original site of
manipulators
Notes: They are welding points of car shell.
And there is a fixed starting point of manipulators.

## Slide 6
One feasible solution
Problem Description
Introduction about this problem
Notes: If there are three manipulators, this is a possible path plan.

## Slide 7
Problem Description
Introduction about this problem
Another feasible solution
Notes: And so does it.
But in this case we can find the blue one welding more points so that it may consume more time to weld.
In contrast, the green one welds few points, it may finish it’s task early and just wait for the blue one.
So it’s not a good path because the max total processing time depends on the max one.

## Slide 8
Problem Description
The information we already know
１
Collision cases should be avoided
There are three manipulators can weld points
２
All points should be welded once
The total number and positions of welding points
３
We can get the travel time between each two points
The moving path between each two points are fixed
Notes: This is the information we already know.
There are 3 manipulators, and each of them has fixed processing range. We should avoid the collision cases.
And then there are fixed welding points, and all of them should be welded.
If we decide to move from point i to point j, there is a fixed moving path.

## Slide 9
Parameters & Variables
02
Notes: The following is parameters and variables

## Slide 10
Parameters & Variables
Limitation of problem in real world
One point can be welded once
Objective is to minimize the max processing time, including the travel time and welding time
One manipulator can weld one point at once
One manipulator can have only one route
Collisions are not allowed
Notes: Before introducing the setting, there are some thing we need to notice.
One point can be welded once
One manipulator can weld one point at once
One manipulator can have only one route
Collisions are not allowed

## Slide 11
Sets
Node : the welding points
Parameters & Variables
Sets, variables and parameters
Arc : possible edges between nodes i and j
Manipulator : the manipulators
Level space : the level spaces 1 to n
Node : all nodes which contains welding points and original point
Level space : the level spaces 0 to n, which contains starting level
Cross edge : crossed edge and
i
j
i'
j'
Notes: Base on the limitations, I define these sets.
Nodes are welding points, and possible paths between edge(i, j) belong to set A.
Manipulator and level space respectively belong to set K and set L.
Set R(i) and set N(k) are designed to make the model more efficient.

## Slide 12
Parameters & Variables
Sets, variables and parameters
Variables
Whether manipulator k is welding point i at level l or not:
If it is welding, ; otherwise,
Whether an edge (i, j) is gone through by manipulator k at level l or not:
If it is gone through, ; otherwise,
Parameters
Travel time between node i and j :
Welding time at node i :
Starting time of edge of manipulator k at level l:
Whether time of manipulator k at level l and k’ at level l’ is crossed or not:
If it is crossed, ; otherwise,
Ending time of edge of manipulator k at level l:
Notes: I use variable xilk to express whether manipulator k is welding point i at level l or not
And variable yijlk to express whether an arc (i, j) is gone through by manipulator k at level l or not
Because we want to avoid the collision case, the time should be taken into consideration.
And the parameters we already know are travel time of each edge and welding time of each node.

## Slide 13
Model Design
03
Notes: The following is model constraints

## Slide 14
Model Design
Level space
Case for 1 manipulator :
Level 0
Level 1
Level 2
Level 3
Level n-1
Level n
Level n+1

## Slide 15
1
2
6
3
9
8
7
4
5
10
-1
1
2
6
3
9
8
7
4
5
-1
10
No Crossed Model
No Crossed with
Time Relaxed Model
Model Design

## Slide 16
Model Design
No crossed allowed
1
2
4
3
5
No Crossed Model
Max processing time
Start from 0
Welded once for points
Welding at most one point at each level for manipulators

## Slide 17
6
7
Node 0
Other nodes
Other nodes
Model Design
No crossed allowed
No Crossed Model
Each manipulator with one route

## Slide 18
8
9
Model Design
No crossed allowed
i
Other nodes
Other nodes
Node i
No Crossed Model
Flow balanced

## Slide 19
Model Design
No crossed allowed
i
Other nodes
Other nodes
No Crossed Model
8
9
Flow balanced

## Slide 20
10
Model Design
No crossed allowed
i
j
i'
j'
i
j
i'
j'
i
j
i'
j'
No Crossed Model
No crossed

## Slide 21
Model Design
No Crossed with Time Relaxed Model
1
2
4
3
5
No Crossed with Time Relaxed Model
Max travel time
Start from 0
Welded once for points
Welding once each level for manipulators

## Slide 22
6
7
Model Design
No crossed allowed
No Crossed with Time Relaxed Model
8
9
Each manipulator with one route
Flow balanced

## Slide 23
Model Design
No crossed allowed
No Crossed with Time Relaxed Model
10
11
12
Ending time at level 0
Starting time
Ending time
0
1
2
3

## Slide 24
Model Design
No crossed allowed
No Crossed with Time Relaxed Model
13
Whether time crossed

## Slide 25
Model Design
No crossed allowed
No Crossed with Time Relaxed Model
14
Whether time crossed
i
j
i'
j'
i
j
i'
j'
i
j
i'
j'

## Slide 26
Results
04
Notes: This is the last chapter

## Slide 27
1
2
6
3
9
8
7
4
5
-1
10
Results
Crossed allowed model
Crossed Allow Model
Opt = 128, running time = 101(s)

## Slide 28
Results
No crossed model
1
2
6
3
9
8
7
4
5
10
-1
No Crossed Model
Opt = 130, running time = 181(s)

## Slide 29
1
2
6
3
9
8
7
4
5
-1
10
Results
No crossed with time relaxed model
No Crossed with Time Relaxed Model
Opt = 128, running time = 374(s)

## Slide 30
Conclusion
1
2
6
3
9
8
7
4
5
10
0
1
2
6
3
9
8
7
4
5
0
10
No Crossed Model
No Crossed with
Time Relaxed Model
Opt = 130, running time = 181(s)
Opt = 128, running time = 374(s)
1
2
6
3
9
8
7
4
5
0
10
Crossed Allow Model
Opt = 128, running time = 101(s)

## Slide 31
Conclusion
Decreasing the processing time can raise up the production capacity per unit time, so that we can meet more demand to get more profit.
Notes: The result of model can find the policy with least processing time.
Decreasing the processing time can raise up the production capacity per unit time, so that we can meet more demand to get more profit.

## Slide 32
Thanks for listening
2020.12.28 Yu-En Shen
Notes: This is my presentation
Thanks for listening